## Slide 1: Application layer
Introduction
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: What is it?
Internet view
everything above the socket interface is application layer function
=> all functions of OSI layers 5 and 6 are Internet application layer
We still need (many of) those OSI functions
long-term session maintenance, reconnections, session migration
protocol translation
Today’s Internet world has protocols for this
  (official standards (de jure) and de facto)
  SMTP + (POP3 or IMAP)
  HTTP, SHTTP, QUIC
  (RTSP or SIP) + RTP/RTCP
  MPEG DASH, Apple HLS, Microsoft Smooth Streaming
  REST, SOAP, DCE / CORBA
Notes:   E.g. RTP realizes some such functions; is part of the Java JDK…
Basically no limits to the functionality of applications => lower-layer functionality can be built on top of the socket interface too (networks on top of networks…)
  Perhaps most obvious for real-time multimedia transmission
Upper-layer functionality can be separated in more and more layers…
What follows: some things to keep in mind when developing an application-layer protocol; some example protocols (SMTP, HTTP)
6 presentation: oversetter formatter
5 session: koblinger som skal leve lenge eller bruke mer kompliserte relasjoner enn transportlaget støtter

## Slide 3: Application layer
Basic interaction patterns
IN2140: Introduction to Operating Systems and Data Communication

## Slide 4: Client-Server
Traditional communication model, easily comprehensible abstraction
  Clients request service (initiate connection)
  Servers provide service (answer requests)
Examples: Web Client/Server, Mail Client/Server, FTP Client/Server
Important: client-server is not request-response

## Slide 5: Publish-Subscribe
Message-dissemination model
  Producer generates messages (initiate connection)
  Consumer receives messages (answer requests)
Producers do not necessarily know consumers
Notification
service

## Slide 6: Peer-to-Peer
Recognized application-layer
paradigm since 2000s
First clearly visible application: Napster
file sharing (mostly for music)
ruled illegal
followed by others: Gnutella, Kazaa, BitTorrent, Freenet
later picked up by research: CAN, Chord, Tapestry, Kademlia, Pastry
idea: avoid control and/or censorship
Famous services
video streaming: PPTV, P2PTV
distributed computing: SETI@home
Old tech. that is like P2P but not recognized:
  Telephony
  Usenet news
  IP Routing
Actually, P2P = original Internet model
all nodes are equal
all nodes can address each other
ownership is distributed

## Slide 7: Application layer
Presentation layer functions
IN2140: Introduction to Operating Systems and Data Communication

## Slide 8: The presentation problem
Q: Does perfect memory-to-memory copy solve “the communication problem”?
A: Not always!
Problem: Different data format, storage conventions
struct Test
{
char code;
int x;
}
Test test;
test.x = 273;
test.code=‘a’
0x61
In memory on e.g. Intel DOS: not packed, little endian
a
.
.
.
0x11
0x01
0x00
0x00
a+1
a+2
a+3
a+4
a+5
a+6
a+7
test.code
Padding
test.x
0x61
a
0x00
0x00
0x01
0x11
.
.
.
a+1
a+2
a+3
a+4
a+5
a+6
a+7
test.code
test.x
Memory not assigned to test
In memory on e.g. ARM Linux: packed, big endian

## Slide 9: Solving the presentation problem
1. Translate local-host format to host-independent format
2. Transmit data in host-independent format
3. Translate host-independent format to remote-host format
Old Style
cross-platform standardized binary encoding of data structures
  OSI host-independent format: “Abstract Syntax Notation One” (ASN.1) defines “Basic Encoding Rules” (BER)
  XDR: „external data representation“, belonged to NFS (Network File System)
Current Style
encoding everything as text
  XML: „extensible markup language“
  REST: „representational state transfer”
convey data in platform-independent manner
local styling and interpretation
readable and debuggable
compensate for platform differences
assume single data interpretation
space-saving
Notes: More recent option: send host-local format with hints, translate if necessary on reception

## Slide 10: XDR example
struct datarate {
long data;
long seconds;
};
bool_t xdr_datarate(XDR* xdrs,
datarate *gp)
{
if (xdr_long(xdrs, &gp->data) &&
xdr_long(xdrs, &gp->seconds))
return(TRUE);
return(FALSE);
}
void program(int socket) {
datarate R = { 1000, 1 };
XDR* p;
xdrmem_create( p, buf, 16, XDR_ENCODE);
xdr_datarate( p, &R );
write( socket, buf, 16 );
}
XDR compiler
C compiler
C compiler
Linker
OS/platform-specific XDR library
OS/platform-specific
program

## Slide 11: REST example
void sendfunction( int socket, datarate* gp ) {
char buf[1000];
sprintf(buf, “POST https://peer.nowhere.com”
“/1/classes/datarate HTTP/1.1\n”
...
“’{\”data\":\”%d\”,\”seconds\":\”%d\”}’/n”
“https://peer.nowhere.com/1/classes”
“/datarate”,
gp->data, gp->seconds );
}
POST https://peer.nowhere.com/1/classes/datarate HTTP/1.1
...
X-Parse-Application-Id: Datarate-Setter
X-Parse-REST-API-Key: JASD3476D
Content-Type: application/json
’{”data":1000,”seconds":”1”}’
https://peer.nowhere.com/1/classes/datarate
struct datarate {
long data;
long seconds;
};
C compiler
Linker
sent over the network at
run-time:

## Slide 12: Application layer
HTTP
Hypertext Transfer Protocol
IN2140: Introduction to Operating Systems and Data Communication

## Slide 13: The Web: the HTTP protocol
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model
  client: browser that requests, receives, “displays” Web objects
  server: Web server sends objects in response to requests
Three major versions
HTTP/1.0 (1990)
HTTP/1.1 (1999)
HTTP/2 (2015)
Host running
a browser
Server
Running
A web
server
Host running
a browser
HTTP request
HTTP request
HTTP response
HTTP response

## Slide 14: The HTTP protocol
HTTP: TCP transport service:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
Protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 15: HTTP example
Suppose user enters URL www.mn.uio.no/ifi/index.html
1a. HTTP client initiates TCP connection to HTTP server (process) at www.mn.uio.no. Port 80 is default for HTTP server.
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket
1b. HTTP server at host www.mn.uio.no waiting for TCP connection at port 80. “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object (ifi/index.html), sends message into socket
time
(now let’s say index.html contains text, references to 10 JPEG images)

## Slide 16: HTTP example (cont.)
5. HTTP client has received response message containing HTML file, displays HTML. Parsing HTML file, finds 10 referenced JPEG objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.
time

## Slide 17: Non-persistent, persistent connections
Non-persistent
HTTP/1.0: server parses request, responds, closes TCP connection
2 RTTs to fetch object
  TCP connection
  object request/transfer
each transfer suffers from TCP’s initially slow sending rate (partly fixed today)
each transfer may finish with delay
many browsers open multiple parallel connections
Persistent
default for HTTP/1.1
on same TCP connection: server, parses request, responds, parses new request,..
client sends requests for all referenced objects as soon as it receives base HTML
fewer RTTs, less slow start
Persistent with pipelining
request multiple objects in one go (even fewer RTTs)
answers arrive one after each other in order of requests
Notes: persistent: varig / bestandig

## Slide 18: HTTP/1.x message format: request
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
GET /ifi/index.html HTTP/1.0
User-agent: Mozilla/4.0
Accept: text/html, image/gif,image/jpeg
Accept-language:no
(extra carriage return, line feed)
request line
(GET, POST,
HEAD commands)
header
lines
Carriage return,
line feed
indicates end
of message

## Slide 19: HTTP/1.x message format: response
HTTP/1.0 200 OK
Date: Thu, 06 Aug 1998 12:00:15 GMT
Server: Apache/1.3.0 (Unix)
Last-Modified: Mon, 22 Jun 1998 …...
Content-Length: 6821
Content-Type: text/html
data data data data data ...
status line
(protocol
status code
status phrase)
header
lines
data, e.g.,
requested
html file

## Slide 20: HTTP/1.x response status code examples
200 OK
  request succeeded, requested object later in this message
301 Moved Permanently
  requested object moved, new location specified later in this message (Location:)
400 Bad Request
  request message not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported

## Slide 21: Trying out HTTP/1.x (client side) for yourself
1. Telnet to your favorite Web server:
Opens TCP connection to port 80
(default HTTP server port) at www.aftenposten.no.
Anything typed in will be sent via this connection.
telnet www.aftenposten.no 80
2. Type in a GET request:
GET / HTTP/1.1
By typing this in (hit carriage
return once), you send
this minimal (but complete)
GET request for the root document to the HTTP server
3. Quickly: type in the host header:
Servers can be multi-homed (multiple different web sites on physical server), and so the client must specify which host it wants. Else, a server would often return an error message.
Host: www.aftenposten.no
4. Hit carriage return twice and see the result

## Slide 22: Cookies: keeping “state”
server-generated # , server-remembered #, later used for:
  authentication
  remembering user preferences, previous choices
server sends “cookie” to client in response msg
  Set-cookie: 1678453
client presents cookie in later requests
  cookie: 1678453
client
server
usual http request msg
usual http response +
Set-cookie: #
usual http request msg
cookie: #
usual http response msg
usual http request msg
cookie: #
usual http response msg
cookie-
spectific
action
cookie-
spectific
action

## Slide 23: Conditional GET: client-side caching
Goal: don’t send object if client has up-to-date cached version
client: specify date of cached copy in http request
  If-modified-since: <date>
server: response contains no object if cached copy is up-to-date:
  HTTP/1.0 304 Not Modified
client
server
http request msg
If-modified-since: <date>
http response
HTTP/1.0
304 Not Modified
object
not
modified
http request msg
If-modified-since: <date>
http response
HTTP/1.1 200 OK
<data>
object
modified

## Slide 24: Web Caches (proxy server)
user sets browser: Web accesses via web cache
client sends all HTTP requests to web cache
  object in web cache: web cache returns object
  else web cache requests object from origin server, then returns object to client
Goal: satisfy client request without involving origin server
client
Proxy
server
client
HTTP request
HTTP request
HTTP response
HTTP response
HTTP request
HTTP response
origin
server
origin
server
Assumption: cache is closer to client (e.g. same network) => faster, less “long-distance” traffic

## Slide 25: Changes in HTTP/2
textual protocol
can be written manually
can be read when intercepted
easy to add (and ignore) proprietary extensions
very talkative
binary protocol
saves space
less data to write and parse
exactly specified
hard to extend
uncompressed header
required in 1.0
avoidance eases transition to 1.1
compressed header
adds a lookup table
may save space
info like: cookies, referer, stream dependencies, weighting, priorities, client identification, ...

## Slide 26: Changes in HTTP/2
ordered and blocking
speed-up by using several parallel TCP connections (1.x)
speed-up by using pipelining (1.1)
multiplexed
send all requests at once
server chooses order (e.g. send advertising inlays first) and can mix messages
GET “body”
GET “img”
GET “img”
GET “css”
get “body”
get “img”
get “img”
get “css”
app-layer flow control per subflow

## Slide 27: Changes in HTTP/2
client pull
assumption: server is stateless
client pull + server push
assumption: server knows best
pipeline
multiplex
server push

## Slide 28: Application layer
SMTP and MIME
Simple mail transfer protocol
Multipurpose Internet mail extensions
IN2140: Introduction to Operating Systems and Data Communication

## Slide 29: Electronic Mail
Major components
  “mail clients” Message User Agents (MUAs)
  “mail servers” Message Submission / Transfer / Delivery Agents (MSA, MTA, MDA)
    often realized as one component called Message Handling Service (MHS)
MUA
  a.k.a. “mail reader”
  composing, editing, reading mail messages
  outgoing, incoming messages stored on server

## Slide 30: Electronic Mail: mail servers
Mail Servers
mailbox contains incoming messages (yet to be read) for user
message queue of outgoing (to be sent) mail messages
Simple Mail Transfer Protocol (SMTP)
between mail servers to send email messages
client: sending mail server
server: receiving mail server
user mailbox
outgoing
message queue
user agents
mail
server
mail
server
mail
server
SMTP
SMTP
SMTP
SMTP
POP3

## Slide 31: Electronic Mail: SMTP
uses TCP to reliably transfer email message from client to server, port 25
direct transfer: sending server to receiving server
three phases of transfer
  handshaking (greeting)
  transfer of messages
  closure
command/response interaction
  commands: ASCII text
  response: status code and phrase
messages must be in 7-bit ASCII

## Slide 32: Sample SMTP interaction
S: 220 hamburger.edu
C: HELO crepes.fr
S: 250 Hello crepes.fr, pleased to meet you
C: MAIL FROM: <alice@crepes.fr>
S: 250 alice@crepes.fr... Sender ok
C: RCPT TO: <bob@hamburger.edu>
S: 250 bob@hamburger.edu ... Recipient ok
C: DATA
S: 354 Enter mail, end with "." on a line by itself
C: Do you like ketchup?
C: How about pickles?
C: .
S: 250 Message accepted for delivery
C: QUIT
S: 221 hamburger.edu closing connection

## Slide 33: Handmade SMTP
telnet servername 25
see 220 reply from server
enter HELO, MAIL FROM, RCPT TO, DATA, QUIT commands
above lets you send email without using email client (reader)

## Slide 34: SMTP: final words
SMTP uses persistent connections
SMTP requires message (header & body) to be in 7-bit ASCII
Certain character strings not permitted in msg (e.g., CRLF.CRLF). Thus msg has to be encoded (usually into either base-64 or quoted printable)
SMTP server uses CRLF.CRLF to determine end of message (no length header)
Comparison with HTTP/1.x:
HTTP: pull
STMP: push
  until final server!
  historical: reading mails stored on server using NFS
both have ASCII command/response interaction, status codes
HTTP
  each object encapsulated in its own response msg
SMTP
  originally the same
  now: multiple objects sent in multipart msg

## Slide 35: Mail message format
SMTP: protocol for exchanging email msgs
Standard for text message format:
header lines, e.g.,
  To:
  From:
  Subject:
  different from SMTP commands!
body
  the “message”, ASCII characters only
header
body
blank
line

## Slide 36: Message format: multimedia extensions
MIME: multipurpose Internet mail extension
additional lines in msg header declare MIME content type
From: alice@crepes.fr
To: bob@hamburger.edu
Subject: Picture of yummy crepe.
MIME-Version: 1.0
Content-Transfer-Encoding: base64
Content-Type: image/jpeg
base64 encoded data .....
.........................
......base64 encoded data
multimedia data
type, subtype,
parameter declaration
method used
to encode data
MIME version
encoded data
“classical” mail may indicate:
Content-type: text/ascii
but 7-bit ASCII text is still the default

## Slide 37: MIME types
Content-Type: type/subtype; parameters
Video
example subtypes: mpeg, quicktime
Application
other data that must be processed by reader before “viewable”
example subtypes: msword, octet-stream
Text
example subtypes: plain, html
Image
example subtypes: jpeg, gif
Audio
example subtypes: basic (8-bit mu-law encoded), 32kadpcm (32 kbps coding)

## Slide 38: Multipart Type
From: alice@crepes.fr
To: bob@hamburger.edu
Subject: Picture of yummy crepe.
MIME-Version: 1.0
Content-Type: multipart/mixed; boundary=98766789
--98766789
Content-Transfer-Encoding: quoted-printable
Content-Type: text/plain
Dear Bob,
Please find a picture of a crepe.
--98766789
Content-Transfer-Encoding: base64
Content-Type: image/jpeg
base64 encoded data .....
.........................
......base64 encoded data
--98766789--
SMTP header
SMTP body
MIME header
MIME body

## Slide 39: Mail access protocols
SMTP: delivery/storage to receiver’s server
Mail access protocol: retrieval from server
  POP: Post Office Protocol
    authorization (agent <==> server) and download
  IMAP: Internet Mail Access Protocol (InterimInteractiveInternet)
    more features (more complex)
    manipulation of stored messages on server
  HTTP: web readers for Outlook, Google mail, etc.
user
agent
sender’s mail
server
user
agent
SMTP
SMTP
POP3 or
IMAP
receiver’s mail
server

## Slide 40: POP3 protocol
authorization phase
client commands:
  user: declare username
  pass: password (plain text!)
server responses
  +OK
  -ERR
transaction phase, client:
list: list message numbers
retr: retrieve message by number
dele: delete
quit
C: list
S: 1 498
S: 2 912
S: .
C: retr 1
S: <message 1 contents>
S: .
C: dele 1
C: retr 2
S: <message 1 contents>
S: .
C: dele 2
C: quit
S: +OK POP3 server signing off
S: +OK POP3 server ready
C: user alice
S: +OK
C: pass hungry
S: +OK user successfully logged on

## Slide 41: IMAP protocol example (from RFC3501)
C: <open connection>
S: * OK IMAP4rev1 Service Ready
C: a001 login mrc secret
S: a001 OK LOGIN completed
C: a002 select inbox
S: * 18 EXISTS
S: * FLAGS (\Answered \Flagged \Deleted \Seen \Draft)
S: * 2 RECENT
S: * OK [UNSEEN 17] Message 17 is the first unseen message
S: * OK [UIDVALIDITY 3857529045] UIDs valid
S: a002 OK [READ-WRITE] SELECT completed
C: a003 fetch 12 full
S: * 12 FETCH (FLAGS (\Seen) INTERNALDATE "17-Jul-1996 02:44:25 -0700"
RFC822.SIZE 4286 ENVELOPE ("Wed, 17 Jul 1996 02:23:25 -0700 (PDT)"
"IMAP4rev1 WG mtg summary and minutes"
(("Terry Gray" NIL "gray" "cac.washington.edu"))
(("Terry Gray" NIL "gray" "cac.washington.edu"))
(("Terry Gray" NIL "gray" "cac.washington.edu"))
((NIL NIL "imap" "cac.washington.edu"))
((NIL NIL "minutes" "CNRI.Reston.VA.US")
("John Klensin" NIL "KLENSIN" "MIT.EDU")) NIL NIL
"<B27397-0100000@cac.washington.edu>")
BODY ("TEXT" "PLAIN" ("CHARSET" "US-ASCII") NIL NIL "7BIT" 3028
92))
S: a003 OK FETCH completed
C: a004 fetch 12 body[header]
S: * 12 FETCH (BODY[HEADER] {342}
S: Date: Wed, 17 Jul 1996 02:23:25 -0700 (PDT)
S: From: Terry Gray <gray@cac.washington.edu>
S: Subject: IMAP4rev1 WG mtg summary and minutes
S: To: imap@cac.washington.edu
S: cc: minutes@CNRI.Reston.VA.US, John Klensin <KLENSIN@MIT.EDU>
S: Message-Id: <B27397-0100000@cac.washington.edu>
S: MIME-Version: 1.0
S: Content-Type: TEXT/PLAIN; CHARSET=US-ASCII
S: DATA
S: )
S: a004 OK FETCH completed
C a005 store 12 +flags \deleted
S: * 12 FETCH (FLAGS (\Seen \Deleted))
S: a005 OK +FLAGS completed
C: a006 logout
S: * BYE IMAP4rev1 server terminating connection
S: a006 OK LOGOUT completed

## Slide 42: IMAP can do more
IMAP capabilities
  create, delete, rename mail folders
  check for new messages, remove messages, set and clear flags
  parse, search, selective fetch
  search WITHIN messages
  STORE and conditional STORE
  CATENATE (to concatenate)
often used for:
  TODOs
  Notes with or without Mime elements
but: replace “message” with “file” and you have a quite complete file system

## Slide 43: Summary
First peek at structure of distributed applications
Presentation Layer functions
Domain Name Systems
  with note on CDNs
HTTP
SMTP
  and an example for POP3 and IMAP